## Slide 1: C & J Series SiPM Technology & Markets
onsemi Depth Sensing
June 2022

## Slide 2: Introduction & Target Markets

## Slide 3: Depth Sensing Division, ISG
SensL Technologies, now Depth Sensing Division, was acquired by ON Semiconductor May 2018
Independent division within Intelligent Sensing Group (ISG) focused on Medical Imaging and LiDAR solutions
Division engineering remains in Cork Ireland
Leveraging resources of all 34,000 ON employees
World HQ
Phoenix, AZ USA
Depth Sensing Division HQ
Cork, Ireland
ISG HQ
Santa Clara, CA USA
ON Semiconductor HQ
Phoenix, AZ
Hassane El-Khoury, CEO
Analog Solutions Group (ASG)
Power Solutions Group (PSG)
Intelligent Sensing Group (ISG)
Industrial & Consumer Solutions Division (ICSD)
Corporate Marketing
Sales
Finance
Mfg/Ops
Corporate R&D
Automotive Sensing Division (ASD)
Depth Sensing Division

## Slide 4: Target Markets Overview
Medical Imaging PET, SPECT, PET-CT, PET-MR, Bone densitometry, Surgical probes
Hazard and Threat Detection Radiation Detection, Contraband Detection, Cargo Scanning, Contamination Monitors
Automotive and Industrial Advanced Driver Assist Systems, Laser Range Finding, Robotic Automation
(likely more relevant to R-Series Products)
Biophotonics
Haematology, Flow Cytometry, DNA Analysis, Continuous Glucose Monitoring

## Slide 5: Established Markets
Medical Imaging
Radiation Detection

## Slide 6: SiPM Technology

## Slide 7: What is a SPAD/SiPM?
Used to time or count photon arrival
Sensitive to single photons from 200nm to 1000nm (silicon)
Critical figures of merit:
  Photon Detection Efficiency (PDE)
  Dark Count
  Gain/Responsivity
  Operating Voltage
  Temperature Coefficient
  Sensor Uniformity
SiPM example created from a 12 microcell SPAD array
Single SPAD based microcell
SPAD/SiPM time or count multiple photons
MicroRB-10020-MLP
SiPM Sensor (1590 element SPAD Array)
Depth Sensing SPAD/SiPM lead in all categories & are widely adopted in multiple markets today
Photons detected by a SPAD
produce a measurable current pulse

## Slide 8: Blue Sensitive SiPM Families
High volume, low noise, MLP package
Highest PDE and timing resolution, TSV package
J-Series
C-Series

## Slide 9: Depth Sensing Division C & J Series SiPM Product Portfolio
C-Series & J Series SiPM
Evaluation
Standard Arrays

## Slide 10: C & J Series Overview

## Slide 11: C-Series SiPMs
Blue sensitive (420 nm peak) SiPM, with high PDE and lowest dark count
  Available in 1 mm, 3 mm and 6 mm sizes
  Various microcell sizes from 10 mm to 35 mm
Robust, low cost MLP package
  Single pixels
  Evaluation board
  Array
  Array breakout board

## Slide 12: J-Series SiPMs
Blue sensitive (420 nm peak) SiPM, with highest PDE and low dark count
  Available in 3 mm, 4 mm and 6 mm sizes
  35 mm cells size
Compact, low dead space TSV package
  Single pixels
  Evaluation board
  Array
  Array breakout board

## Slide 13: SiPM Array Technology

## Slide 14: C-Series SMT Array Variants
Available for rapid testing
  8x8 of 1mm SMT/MLP
    1.7mm pitch
  4x4 of 3mm SMT/MLP
    4.2mm pitch
  12x12 of 3mm SMT/MLP
    4.2mm pitch
  8x8 of 6mm SMT/MLP
    7.2mm pitch
Passive Breakout Board (BoB)
  Ability to readout any pixel
  3 SMA connection options
Full Reference Design Available
8x8 of 1mm (2.49 cm2)
4x4 of 3mm (2.74 cm2)
12x12 of 3mm (25.2 cm2)
8x8 of 6mm (32.94 cm2)
2x2 array of
6x6mm MLP

## Slide 15: J-Series TSV Array Variants
Available for rapid testing
  8x8 of 3mm TSV
    3.3mm pitch
  4x4 of 3mm TSV
    3.3mm pitch
  2x2 of 6mm TSV (BGA & pin)
    6.3mm pitch
  8x8 of 6mm TSV
    6.3mm pitch
Passive Breakout Board (BoB)
  Ability to readout any pixel
  Summed variant available
  4x4 of 3mm TSV
  8x8 of 3mm TSV
  8x8 of 6mm TSV
  2x2 of 6mm TSV (BGA & pin variants)

## Slide 16: C-Series, J-Series, R-Series PDE Comparison

## Slide 17: Sample Applications for C & J Series

## Slide 18: Biophotonic Applications
Depth Sensing division detectors are attractive to numerous biophotonic analysis applications where legacy detectors are unsuited, including:
  Flow cytometry
  Continuous glucose monitoring (CGM)
  Blood oxygen (pulsed oximeter) systems
  Kidney function monitors
  Fluorescence analysis
  Luminometers
  Particulate analysis
  DNA analysis
  Retinal Scanning
  Microscopy

## Slide 19: Gamma Radiation Detection
SPRD – Spectroscopic Portable Radiation Detector
  Based on scintillation detector – CsI(Tl), NaI(Tl), CeBr3 crystal etc + photodetector
    Some models based on CZT (direct detection)
    Some include He3-based systems or Li-6 scintillation materials for simultaneous neutron detection
  Required energy range – from around 30keV to around 3 MeV typically
  Temp operating range -20C to +50C typically
  CZT systems can provide around 3.5% FWHM at 662keV, but CsI(Tl) are around 6-7% FWHM typically
  Wireless connectivity often use, long battery life desirable
  Several examples of typical SPRDs are shown below

## Slide 20: Cancer Detection - Positron Emission Tomography (PET)
Market Trend: SiPMs are replacing old Photomultiplier Tube (PMT’s) in all new PET designs
Major design win with leading Chinese medical imaging customer, United Imaging Healthcare

## Slide 21: PET Detector Block
Array of SiPMs
30,000 SiPMs are in a full body PET scanner

## Slide 22: Medical Imaging
World’s first total-body PET/CT system
  UC Davis, LBNL, U Penn
  5 year, $15.5M program awarded 2015
Industry partners announced January 2017
  United Imaging Healthcare
  SensL Technologies / ON Semiconductor
Depth Sensing Division Sensors
  MicroFJ-30035-TSV
  53,760 SiPM
First human scan in Sept 2018
Nature article over published June 2019

## Slide 23: Key SiPM Parameters for Nuclear Imaging
High PDE at the desired wavelength
  More efficient photon detection reduces timing uncertainty
Signal rise time and recovery time
  Short rise time for better CRT
  Faster recovery time for DR and to allow high event rate (NEMA standard)
Low noise
  Excess noise affects energy resolution and CRT
Package and form factor
  Sensor or array size should match scintillator dimensions
  SiPM must be optically coupled to scintillator
Temperature stability
C-Series SiPM
J-Series SiPM
SiPM Arrays
Products for Nuclear Imaging

## Slide 24: Quality & Reliability

## Slide 25: SiPM Shipment – Tape & Reel
1mm MLP
3mm MLP
6mm MLP
All parts shipped as tape and reel in moisture barrier bag to J-ST 033
MSL=3 reflow solder compliant
All parts ship 3000 units per tape
  1mm on 7” diameter (8mm width)
  3mm on 13” diameter (12mm width)
  6mm on 13” diameter (16mm width)
Full SMT Handling Guide & Array Reference Design available
J-Series now shipping on Tape & Reel
Tape & Reel
Cut Tape

## Slide 26: SPIE Publication
Citation:
Carl Jackson ; Kevin O’Neill ; Liam Wall and Brian McGarvey "High-volume silicon photomultiplier production, performance, and reliability", Opt. Eng. 53(8), 081909 (Aug 15, 2014). http://dx.doi.org/10.1117/1.OE.53.8.081909

## Slide 27: Reliability Test of Silicon
All stress and test steps were carried out as per Joint Electron Device Engineering Council (JEDEC) standard conditions – JESD22-A108D “Temperature, bias and operating life”

## Slide 28: Additional SiPM Temperature Stress Details
1000hr @ 85˚C
1000hr @ 105˚C
No change in optical performance for 85˚C and 105 ˚ C 1000hr temperature stress.
All data within PDE measurement system error.

## Slide 29: Evaluation Boards & Documentation

## Slide 30: C & J-Series SMA / SMTPA Test Boards
J-Series SMA Test Board
C-Series SMTPA Test Board
3x3mm Sensors

## Slide 31: Useful Application Notes
Building Arrays of SiPM Array Readout Methods Scintillator Coupling