## Slide 1: FAN73912, FAN73912A – 1200V Half-Bridge, High & Low side Gate Driver IC
2022

## Slide 2: Contents
1. 1 Pager & Comparison table
2. Key Features and Applications
3. Pin Configuration
4. Typical Application Circuit
5. Timing Diagram
6. Shoot-Through Prevention
7. Advanced Input Filter (HIN,LIN)
8. Promotion Tool [EVB]
9. Benchmarking vs. I-Product
10. What is Considering points for COM-VSS Immunity?
11. Design recommendation
Appendix : Test condition for COM-VSS Immunity

## Slide 3: FAN73912 : 1200 V 2A/-3A Half-bridge Gate Driver IC
The FAN73912 is a monolithic half bridge gate-drive IC designed for high-voltage and high-speed driving for MOSFETs and IGBTs that operate up to +1200 V
  Separate logic supply(VDD) from 3 V to 20 V
  Built-in advanced input filter
  Shoot-through prevention
Strong immunity for dVs/dt
Adjustable input threshold
Reliable design
Gate driver supply(VCC) range from 12 V to 20 V
Cycle-by-cycle edge-triggered shutdown logic
UVLO functions for VDD/VBS
Matched propagation delay below 50 ns
Outputs in-phase with input signal
Logic and power ground +/- 10 V offset
Typical 330ns dead-time
Industrial Motor Driver
UPS & Solar Inverter
Ballast
Half-bridge Converter
FAN73912MX : SOICW-16

## Slide 4: FAN73912A : 1200 V 2A/-3A High & Low Side Gate Driver
The FAN73912A is a monolithic high and low-side gate-drive IC designed for high-voltage and high-speed driving for MOSFETs and IGBTs that operate up to +1200 V
  Separate logic supply(VDD) from 3 V to 20 V
  Built-in advanced input filter
  W/O Shoot-through prevention
Strong immunity for dVs/dt
Adjustable input threshold
Reliable design
Electrical Contactor
Industrial Motor Driver
UPS & Solar Inverter
Ballast
Half-bridge Converter
FAN73912AMX : SOICW-16
SOICW-16
Gate driver supply(VCC) range from 12 V to 20 V
Cycle-by-cycle edge-triggered shutdown logic
UVLO functions for VDD/VBS
Matched propagation delay below 60 ns
Outputs in-phase with input signal
Logic and power ground +/- 10 V offset

## Slide 5: Comparison Table
 | Competitor (Referenced to TA@25℃) | FAN73912A (Referenced to TJ@Full Temp) | FAN73912 (Referenced to TA@25℃)
Max TJ | 125 ℃ | 150 ℃ | 
VB-GND [V] | Max 1225 @ TA=25℃ | Max 1225 @ TJ=25℃ Max 1225 @ TJ=150℃ Max 1100 @ TJ=-40℃ | 
Advanced Input filter | NO | Yes (Typ 150ns) | 
Shoot-Through Prevention | NO | NO | Yes
IO+/IO- [A] | Typ 2.0 / -2.5 | Typ 2.0 / -3.0 | 
VCCUV- / VBSUV- [V] | 7.9/9.3/10.7 | 9.2/10.5/11.4 | 
VCCUV+ / VBSUV+ [V] | 8.7/10.2/11.7 | 9.7/11.0/12.0 | 
VCCUVH/ VBSUVH [V] | Typ 0.9 | Typ 0.5 | 
ILK [uA] | Max 50 | Max 100 | Max 50
IQCC [uA] | Typ 180/ max 340 | Typ 170/ max 350 | Typ 170/ max 300
IQDD [uA] | Typ 15/max 30 | Max 20 | Max 10
IQBS [uA] | Typ 125 / max 130 | Typ 50 / max 100 | 
Separate Power and Logic Ground [V] | Yes (+/- 5V offset) | Yes (+/- 10V offset) | 
Logic input voltage [V] (HIN, LIN and SD) | Min VSS | Min VSS+VDD-20 | 
Negative Vs [V] | -5V | 8-VCC | 
T on propagation delay [ns] | Typ 280 | Typ 500 (influenced by Advanced input filter) | 
Toff propagation delay [ns] | Typ 225 | Typ 550 (influenced by Advanced input filter) | 
Similar Spec.
Differentiated Spec.
Blue : Better Spec.
※ All voltage parameters are absolute voltages referenced to COM unless otherwise specified.
 | Competitor | FAN73912A
Qual Level | Industrial | Industrial
MSL | 3 | 3
Output Phase | In Phase with Input | In Phase with Input
Package | 16 Wide-SOP | 16 Wide-SOP
Channels | 2 | 2
Two stage turn-on for di/dt control | NO | NO
Shoot-Through Prevention | NO | NO
Shut down | YES | YES
VDD for Logic supply | YES | YES
VIH @ VDD=15V [V] | Min 9.5 | Min 9.5
VIL @ VDD=15V [V] | Max 6.0 | Max 6.0

## Slide 6: 2-1. FAN73912 Key Feature and Applications
Block Diagram
Key Features
1200V Off-set
Typically IO+ 2A/ IO- 3A Capability for Both Channels
Gate Driver Supply (VCC) Range from 12 to 20V
Separate Logic Supply(VDD) Range form 3V to 20V
Cycle-by-Cycle Edge-Triggered Shutdown Logic
UVLO Functions for VDD/VBS
Built-in Advanced Input Filter (typ 250ns)
Matched Propagation Delay Below 50ns
Outputs in-Phase with Input Signal
Logic and power ground +/- 10V offset
Shoot-Through Prevention
Applications
Industrial Motor Driver
UPS & Solar Inverter
Ballast
Half-bridge Converter

## Slide 7: 2-2. FAN73912A Key Feature and Applications
Block Diagram
Key Features
1200V Off-set
Typically IO+ 2A/ IO- 3A Capability for Both Channels
Gate Driver Supply (VCC) Range from 12 to 20V
Separate Logic Supply(VDD) Range form 3V to 20V
Cycle-by-Cycle Edge-Triggered Shutdown Logic
UVLO Functions for VDD/VBS
Built-in Advanced Input Filter (typ 250ns)
Matched Propagation Delay Below 50ns
Outputs in-Phase with Input Signal
Logic and power ground +/- 10V offset
Applications
Electrical Contactor
Industrial Motor Driver
UPS & Solar Inverter
Ballast
Half-bridge Converter

## Slide 8: 3. FAN73912 & FAN73912A Pin Configuration
※ Same Pin configuration

## Slide 9: 4. Typical Application Circuit
Symbol | Parameter | Condition | Min. | Typ. | Max. | Unit
VIH | Logic "1" input voltage | VDD=3V | 2.4 |  |  | V
 |  | VDD=15V | 9.5 |  |  | 
VIL | Logic "0" Input Voltage | VDD=3V |  |  | 0.8 | V
 |  | VDD=15V |  |  | 6.0 | 
[Table 1] VDD vs. Input threshold
※Definition for VCC and VDD
VCC: L/S supply voltage of which range is from 12 to 20V. VCC determine the gate driving voltage of IGBT.
VDD: A separated logic supply voltage of which range is from 3 to 20V. VDD determine the threshold level of input signal.

## Slide 10: 5-1. FAN73912 Timing Diagram
※ Cycle-by-Cycle Edge-Triggered Shutdown
: After shutdown input is fallen, output drivers keep low until the next Input transition
(Forced Shutdown)

## Slide 11: 5-2. FAN73912A Timing Diagram
※ Cycle-by-Cycle Edge-Triggered Shutdown
: After shutdown input is fallen, output drivers keep low until the next Input transition
( Forced Shutdown )

## Slide 12: 6. FAN73912 Shoot-Through Prevention
The shoot-through protection circuitry prevents both high- and low-side switches from conducting at the same time, as shown below figure

## Slide 13: 7. FAN73912 & FAN73912A Advanced Input Filter
i) IN pulse-width exceeds tFILTIN
ii) IN pulse-width is less than tFILTIN
Once the IN pulse-width exceeds input filter time, the OUT pulse-width matches the IN pulse-width.

## Slide 14: 8. Promotion Tool [EVB]

## Slide 15: 9. Benchmarking vs. I-Product : DC Negative VS
※ Allowable negative VS voltage of FCS HVIC is lower about -3.5V compared to I-Product.
 | FAN73912, FAN73912A |  | I-Product
VHN [10V/div] VB [10V/div] VS [10V/div] VHO [10V/div] 1ms/div |  | VHN [10V/div] VB [10V/div] VS [10V/div] VHO [10V/div] 1ms/div | 
-9.4V
-6.2V

## Slide 16: 9. Benchmarking vs. I-Product : Negative VS Pulse (NPSOA) @ HIN =0V
Note
Transient negative Vs SOA characteristic was only bench test result.
Chart: Negative VS transient SOA (NPSOA)
| 50 | 100 | 150 | 200 | 250 | 300
FAN73912 EVT0 | -206 | -203 | -189 | -161 | -141 | -126
IR2213 | -94 | -62 | -51 | -45 | -40 | -36
※“Negative Vs” is measured Value
I-Product
FAN73912, FAN73912A
Tested by
ONSEMI Lab

## Slide 17: 9. Benchmarking vs. I-Product : Negative VS Pulse Immunity @ HIN Switching ( W/O BSD, CBOOT: 0.1uF)
Note
Transient negative Vs SOA characteristic was only bench test result.
※“Negative Vs” is measured Value
Chart: Comparison of Negative Vs Pulse Characteristics
| 50 | 100 | 150 | 200 | 250 | 300
IR2213 | -7.7 | -7.5 | -7.3 | -7.3 | -7.2 | -7
FAN73912 EVT2 | -33.5 | -31.2 | -25.2 | -21.9 | -18.3 | -10.6
I-Product
FAN73912, FAN73912A
Better Ruggedness
Tested by ONSEMI Lab

## Slide 18: 9. Benchmarking vs. I-Product : Negative VS Pulse Immunity @ HIN Switching (W/ BSD + 10Ω, CBOOT: 0.1uF)
Note
Transient negative Vs SOA characteristic was only bench test result.
Chart: Comparison of Negative Vs Pulse Characteristics
| 50 | 100 | 150 | 200 | 250 | 300
IR2213 | -8.3 | -8.5 | -8.2 | -8.6 | -8.2 | -8.1
FAN73912 EVT0 | -37.8 | -33.5 | -36.1 | -37.3 | -37.9 | -26.5
VBS=20V | -29.3 | -29.2 | -28.6 | -27.2 | -21.9 | -17
Tested by
ONSEMI Lab
※“Negative Vs” is measured Value
I-Product
FAN73912, FAN73912A
Better Ruggedness

## Slide 19: 9. Benchmarking vs. I-Product : VDD Swing Test (VDD : 0 ~15V)
VHIN =0V VLIN = 5Vp-p 20khz | FAN73912, FAN73912A NO Error | I-PRODUCT LO high @ VDD < 1.0V
VDD [5V/div] VLIN [5V/div] VHO [10V/div] VLO [10V/div] 20ms/div |  | 
VLIN =0V VHIN = 5Vp-p 20khz | FAN73912, FAN73912A NO Error | I-PRODUCT HO high @ VDD < 1.1 V
VDD [5V/div] VHIN [5V/div] VHO [5V/div] VLO [10V/div] 20ms/div |  | 

## Slide 20: 9. Benchmarking vs. I-Product : COM-VSS immunity test
※ All voltages are referenced to VSS unless otherwise noted.
COM Swing Test
COM Pulse test
COM waveform
COM Waveform
Test Result
Test Result
VDD | VPEAK of COM | Output Behavior | 
 |  | FAN73912, FAN73912A | I-Product
3V | 0~3.7V | H/S : Normal L/S : Normal | H/S : Normal L/S : Normal
 | > 3.7V | H/S : OFF L/S : OFF | H/S : OFF, Short-on, Latch-on L/S : Normal
5V | 0~5.6V | H/S : Normal L/S : Normal | H/S : Normal L/S : Normal
 | > 5.6V | H/S : OFF L/S : OFF | H/S : OFF, Short-on, Latch-on L/S : Normal
10V | 0~10.7V | H/S : Normal L/S : Normal | H/S : Normal L/S : Normal
 | > 10.7V | H/S : OFF L/S : OFF | H/S : OFF, Short-on, Latch-on L/S : Normal
VDD | VPEAK of COM | Output Behavior | 
 |  | FAN73912, FAN73912A | I-Product
3V | 0~4V | H/S : Normal L/S : Normal | H/S : Normal L/S : Normal
 | 4~6V | H/S : Normal L/S : Normal | H/S : Latch-on L/S : Normal
 | > 6V | H/S : OFF L/S : Normal | H/S : Latch-on L/S : Normal
5V | 0~6V | H/S : Normal L/S : Normal | H/S : Normal L/S : Normal
 | 6~19V | H/S : Normal L/S : Normal | H/S : Latch-on L/S : Normal
 | > 19V | H/S : Normal L/S : OFF | H/S : Latch-on L/S : OFF
10V | 0~11V | H/S : Normal L/S : Normal | H/S : Normal L/S : Normal
 | 11~21V | H/S : Normal L/S : Normal | H/S : Latch-on L/S : Normal
 | =21V | H/S : Normal L/S : Normal | H/S : Latch-on L/S : OFF

## Slide 21: 10. What is Considering points for COM-VSS immunity?
If a shunt resistor is applied to system as shown in [Figure 1], It may happen that COM voltage exceeds VDD referenced to VSS during over-current status. At this time, the FAN73912, FAN73912A turns off the output without shoot-through events, which can prevent breakdown of the system.
Considering point
: Is VCOM higher than VDD?
Chart: COM- VSS (TJ =25℃)
[Figure 1] Circuit using R_shunt
[Figure 2] I-V Curve @ VCOM > VSS

## Slide 22: 11. Design recommendation
Common-grounded power supplies, VDD, are used for MCU and FAN73912, FAN73912A product operation.
The MLCC placed between VDD-VSS (C1) and VCC-COM(C2) should be over 100nF and mounted as close to the pins of the FAN73912, FAN73912A product as possible.
The bootstrap capacitor (CBOOT) uses a low-ESR capacitor such as ceramic capacitor. The capacitor from VDD to COM (C3) supports both the low-side driver and bootstrap recharge, The recommended value C3 is higher than the recommended CBOOT at least ten times.
Gate Resistors (R1~R4) should be check whether it is suitable for switching characteristics in accordance with IGBTs or MOSFETs
Shunt Resistor, RSHUNT is related with trip level of over current. (Equation: ITRIP = VTRIP/ RSHUNT )
The layout for minimizing parasitic inductances are required.
※ For further details, see the datasheet and application note (AN-6076)

## Slide 23: Appendix : Test condition for COM-VSS Immunity
Test Circuit
Test Condition
TA : 25+/- 3℃
VCC: 15VDC
VDD: 3~10V
HIN : 20khz, 50%, 0~VDD
LIN : Inverted HIN, 0~VDD
COM : Triangle wave (3ms Period, 50% duty 0 ~ 15V) or
Square wave (15khz, 2us pulse width 0~20V)
※ Note : All voltages are referenced to VSS unless otherwise noted.