## Slide 1: SiC Fighting Guide
January 2023

## Slide 2: Si vs. SiC – Silicon Carbide Drives Increased Power Density!
Higher Switching Frequency
System
Small Size
Light Weight
Cost benefits
Simpler topology : higher BVdss with lower Rds(on)
Higher Efficiency by Lower Power Losses
Smaller passives
Smaller heatsink and packaging
Fewer Cooling
SiC
Solution
Si
Solution
Notes: During many year, to overcome low performances of high voltage silicon, stacked or complex structure have been used. SiC devices have high voltage breakdown capability with much lower losses than regular Silicon devices. Using SiC devices simplify high-voltage and high-power design by simplifying topologies.
SiC Switching speed allows high frequency operation for the same application power rating. The direct consequence is the reduced size of passive like inductors and capacitors. With less devices and less losses, the need in cooling is lower and heatsink size is reduced.
All of those improvement lead to a smaller system size for same or better performances.

## Slide 3: Advantages of onsemi EliteSiC technology
Proven Quality / Robust Planar Design
  In-process Control and Burn-in
  Defect Scanning during Manufacturing
  100% Avalanche testing of All Dies
  No Drift in Threshold or Parameters
  High Reliability Gate Oxide
  Automotive Qualification AECQ-100
Best in class design tools
  Physical & Scalable accurate Simulation Models
  Application notes and Design guides
Fully Integrated Manufacturing
  Form Powder to Products
New 3rd generation SiC offering
  Optimized for High temperature operation
    Diodes : Low series-resistance temperature dependency
    MOSFETs : Stable reverse recovery over temperature
  Improved parasitic capacitances for High Frequency High Efficiency application
  Large die with low RDS(on) available
Automotive or Industrial grade for All Values and Packages
Wide offering in Standard and Custom Power Integrated Modules (PIM)
Large portfolio of Voltages and RSD(on) available in 3- and 4-Leads packages
Notes: Here : 2 Options.
Just a brief summary because all points will be detailed in the next slides
onsemi puts a lot of effort to ensure SiC devices reliability and robustness. A lot of action has been taken like defect scanning, in-process control and burn-in, …
onsemi invests in a new modeling technic and tools to facilitate SiC adoption by customers.
onsemi is a full integrated manufacturer form the wafer to the devices.
The third generation of Diodes and MOSFETs are currently released with improved performances dedicated for high frequency operation.
onsemi offers both grade (automotive and industrial) for all device values.
onsemi SiC products are available in various discrete packages or modules with a large range of on-resistance values.
2) Full details in one slide and others detailed slides are not shown…
To insure SiC quality, onsemi puts many controls during the full manufacturing process. During device design, parameters have been measured and checked to have almost no drift and stable performance within temperature and lifetime. onsemi took a particular attention to the reliability of its gate oxide. onsemi gate oxide is robust and withstand very high dv/dt link to SiC devices operating conditions. To catch and remove bad parts, defect scanning is used during manufacturing. At the end of the manufacturing process, a burn-in complete this approach to eliminate all possible remaining bad parts. All dies, devices or modules are fully tested before shipment even in extreme condition like avalanche. Parts for both standard Industrial and Automotive are made with the same design and test requirements. Some production lines are automotive qualified and produce parts with AECQ-100 certification.
onsemi offers best in class tools to help and facilitate customers designs. onsemi invests a lot of effort in creating very accurate simulation models using Silicon Carbide physical equations embedded in those models. onsemi has published many application notes and design guides to teach customers how to use SiC devices. A new online simulation platform will also be available early next year.
onsemi has an integrated manufacturing chain from the sand to the system solutions. It insures onsemi supply impedance and quality.
The new third diodes and MOSFETs generation offer much more optimized performances over temperature. Diodes equivalent series resistor is smaller and less affect by temperature variation. MOSFET body diode reverse recovery is now almost independent of temperature. With reduced parasitic capacitors, new MOSFET generation can operate at high frequency with much less losses than previous generation. Large die with very low on-resistance are available and demonstrate onsemi capability to master technology performances and soldering quality.

## Slide 4: onsemi EliteSiC Leadership: From Substrate to Systems
Substrates / Epi
Fab
Devices / Die
Modules
Systems
SiC Planar available today
200mm migration ready
150/200mm SiC wafering & epi fully internal in onsemi today
Fabs ready today for 150mm→200mm migration
Full portfolio of diodes & MOSFETs
Broad base of packages
Die only & metal options
Auto & Industrial devices
Case & transfer molded options
Full portfolio of hybrid & full SiC modules
Single & dual cooling, direct & indirect
Deep application & system know-how for automotive & industrial
EMEA, US, Asia based apps support
Working on trench for the future
Notes: onsemi has an integrated manufacturing chain from the sand to the system solutions. onsemi has its own SiC boule and wafer production. Then, onsemi design its own diode or MOSFET cell structures. onsemi manufactures dies using this cell structure on 6 inches and migrate to ! Inches wafer. Then, those dies are encapsulated in discrete and module package and tested inside onsemi manufacturing plans. Deep application knowledge and system know-how coming form application engineering team are shared by onsemi in various forms like application notes, seminars, tutorials available online but also with local support team.

## Slide 5: onsemi EliteSiC vertical integration – Unique for the industry
Notes: This completed Silicon Carbide integration is also explained here with the various steps involved from the silicon and carbide powder to the application. The major steps are growing the boule in the furnace, slicing wafers, making the epitaxy layer, wafer diffusion, wafer dicing and dies packaging.

## Slide 6: onsemi EliteSiC >>> Proven Quality & Robust Planar Design
  In-process Control and Burn-in
  Defect Scanning during Manufacturing
  100% Avalanche testing of All Dies
  No Drift in Threshold or Parameters
  High Reliability Gate Oxide
  Automotive Qualification AECQ-100
Real SiC crystals have defects
Contaminants in gate oxide
No drift in Threshold and Gain
Avalanche Capability
Burin-In Climatic chamber
Notes: To insure SiC quality, onsemi puts many controls during the full manufacturing process. During device design, parameters have been measured and checked to have almost no drift and stable performance within temperature and lifetime. onsemi took a particular attention to the reliability of its gate oxide. onsemi gate oxide is robust and withstand very high dv/dt link to SiC devices operating conditions. To catch and remove bad parts, defect scanning is used during manufacturing. At the end of the manufacturing process, a burn-in complete this approach to eliminate all possible remaining bad parts. All dies, devices or modules are fully tested before shipment even in extreme condition like avalanche. Parts for both standard Industrial and Automotive are made with the same design and test requirements. Some production lines are automotive qualified and produce parts with AECQ-100 certification.

## Slide 7: onsemi EliteSiC >>> Best in Class SiC design tools
Best in class design tools
  Physical & Scalable accurate Simulation Models
  Application notes and Design guides
  New online System design tool
    Available soon – will be dynamic and include parasitics and peak currents impacts in loss projections !
Physical Structure
Physical & Scalable Model
Notes: onsemi offers best in class tools to help and facilitate customers designs. onsemi invests a lot of effort in creating very accurate simulation models using Silicon Carbide physical equations embedded in those models. onsemi has published many application notes and design guides to teach customers how to use SiC devices. A new online simulation platform will also be available early next year.

## Slide 8: onsemi EliteSiC >>> Benefits of 3rd Generation SiC technology
New 3rd generation SiC offering
  Optimized for High temperature operation
    Diodes : Low series-resistance temperature dependency
    MOSFETs : Stable reverse recovery over temperature
  Improved parasitic capacitances for High Frequency High Efficiency application
  Large die with low RDS(on) available
Chart: Output Capacitance, Coss [pF]
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600
M3 | 4844 | 4726 | 4608 | 4485 | 4359 | 4240 | 4127 | 4023 | 3925 | 3838 | 3235 | 2900 | 2659 | 2431 | 2071 | 1627 | 1148 | 1035 | 990 | 949 | 913 | 883 | 855 | 831 | 807 | 786 | 766 | 749 | 733 | 663.8 | 612.3 | 571.4 | 535.0528 | 507.6087 | 484.1285 | 446.0017 | 415.7881 | 391.3504 | 370.963 | 353.5105 | 293.5423 | 257.5024 | 232.4541 | 213.8537 | 199.1804 | 187.0236 | 176.9794 | 169.0462 | 162.52 | 156.6975
M1 | 7324 | 7107 | 6891 | 6672 | 6460 | 6254 | 6051 | 5860 | 5677 | 5503 | 4259 | 3730 | 3435 | 3215 | 3037 | 2884 | 2746 | 2611 | 2413 | 2147 | 1842 | 1649 | 1564 | 1508 | 1464 | 1423 | 1386 | 1351 | 1320 | 1193 | 1095 | 1021 | 953.9197 | 903.8085 | 860.9039 | 791.5331 | 736.5268 | 691.0488 | 654.052 | 622.2652 | 514.2908 | 448.8322 | 403.9713 | 370.5594 | 344.535 | 323.4651 | 306.1334 | 291.4273 | 278.8407 | 269.1767
M1
M3S
Chart: Input Capacitance, Ciss [pF]
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600
M3 | 4660 | 4595 | 4537 | 4481 | 4430 | 4384 | 4341 | 4303 | 4267 | 4234 | 4017 | 3910 | 3839 | 3778 | 3697 | 3476 | 3461 | 3455 | 3450 | 3446 | 3442 | 3439 | 3435 | 3433 | 3431 | 3429 | 3425 | 3423 | 3423 | 3408 | 3402 | 3395 | 3383.4857 | 3381.3181 | 3381.3181 | 3380.2343 | 3378.0669 | 3373.7323 | 3373.7323 | 3370.4817 | 3362.8978 | 3357.4816 | 3353.1491 | 3347.7341 | 3343.4026 | 3339.0716 | 3335.8236 | 3330.4108 | 3327.1634 | 3322.834
M1 | 6346 | 6230 | 6113 | 5992 | 5871 | 5748 | 5628 | 5511 | 5397 | 5290 | 4521 | 4301 | 4229 | 4191 | 4161 | 4141 | 4120 | 4104 | 4080 | 3984 | 3931 | 3916 | 3909 | 3905 | 3902 | 3901 | 3898 | 3895 | 3894 | 3880 | 3873 | 3870 | 3855.3671 | 3852.0799 | 3849.8885 | 3846.6017 | 3842.2196 | 3835.6474 | 3832.3616 | 3827.981 | 3813.7471 | 3800.6123 | 3787.4815 | 3778.7299 | 3766.6993 | 3759.0452 | 3751.3924 | 3741.5552 | 3736.091 | 3726.2573
M1
M3S
Chart: Reverse Capacitance, Crss [pF]
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 60 | 70 | 80 | 90 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600
M3 | 1833 | 1769 | 1708 | 1641 | 1573 | 1509 | 1447 | 1392 | 1339 | 1291 | 974 | 826 | 730 | 635.8 | 477.8 | 289.3 | 100.5 | 64.53 | 59.9 | 56.49 | 53.72 | 51.41 | 49.43 | 47.69 | 46.15 | 44.78 | 43.56 | 42.45 | 41.43 | 37.42 | 34.51 | 32.01 | 29.7007 | 28.6299 | 27.7694 | 26.3484 | 25.2477 | 24.3372 | 23.5667 | 22.8864 | 20.5251 | 19.0044 | 17.9539 | 17.1436 | 16.5033 | 15.9931 | 15.5629 | 15.2028 | 14.9227 | 14.6726
M1 | 3093 | 2963 | 2827 | 2687 | 2546 | 2412 | 2279 | 2145 | 2016 | 1893 | 1033 | 770 | 679 | 625.6 | 586.2 | 553.9 | 524.8 | 493.2 | 427.5 | 329.2 | 214.7 | 142.6 | 120.8 | 113.2 | 108.6 | 104.7 | 101.3 | 98.4 | 95.5 | 85.4 | 78.5 | 73.3 | 68.2164 | 65.0313 | 62.3972 | 58.121 | 54.8265 | 52.143 | 49.9102 | 48.008 | 41.5109 | 37.4971 | 34.7146 | 32.6329 | 30.9816 | 29.6507 | 28.5499 | 27.6393 | 26.8888 | 26.4185
M1
M3S
M3
Almost T-independent
Reverse Recovery
Notes: The new third diodes and MOSFETs generation offer much more optimized performances over temperature. Diodes equivalent series resistor is smaller and less affect by temperature variation. MOSFET body diode reverse recovery is now almost independent of temperature. With reduced parasitic capacitors, new MOSFET generation can operate at high frequency with much less losses than previous generation. Large die with very low on-resistance are available and demonstrate onsemi capability to master technology performances and soldering quality.

## Slide 9: Competitive analysis (January 2023)
Eon losses (mJ) vs Drain Current :
Eoff losses (mJ) ve Drain Current
Chart: 
| 10.9 | 22.1 | 32.82 | 42.99 | 53.12 | 63.36 | 72.75 | 81.78 | 91.04
 | 0.14 | 0.29 | 0.45 | 0.63 | 0.84 | 1.06 | 1.28 | 1.54 | 1.8
 | 0.29 | 0.5 | 0.73 | 0.95 | 1.2 | 1.44 | 1.69 | 1.95 | 2.23
 | 0.17 | 0.29 | 0.42 | 0.56 | 0.71 | 0.87 | 1.04 | 1.24 | 1.43
Test setup : Standard double pulse test
  Inductive load
  Free welling diode : 50A onsemi D3 1200V SiC Diode in TO247
  SiC Mosfet 1200V
  Driver – NCD57000 with Bipolar Buffer
  Rg = 8.2/8.2Ω
  Vdc = 600V
  Vgs = (+15 / -5V)
  Temp = 125°C
  Current transformer ID measurement
  Ls ~ 30nH
Chart: 
| 10.9 | 22.1 | 32.82 | 42.99 | 53.12 | 63.36 | 72.75 | 81.78 | 91.04
 | 0.05 | 0.07 | 0.13 | 0.2 | 0.28 | 0.38 | 0.48 | 0.59 | 0.7
 | 0.07 | 0.13 | 0.22 | 0.32 | 0.44 | 0.56 | 0.69 | 0.83 | 0.97
 | 0.05 | 0.07 | 0.11 | 0.18 | 0.25 | 0.34 | 0.43 | 0.53 | 0.65
NTH4L022N120M3S – onsemi 22mW M3S
Competitor A – 1200V 21mW (Last generation)
Competitor B – 1200V 20mW (Last generation)
Notes: Due to very good performances of onsemi M3S MOSFET body diode reverse recovery over the full temperature range, onsemi M3S new EliteSiC 22 milli-Ohms MOSFET exhibits lower switching losses on a standard double pulse tester over the full drain current range. Both turn-on and turn-off losses are better. Total losses at maximum current are 20% lower with onsemi new M3S EliteSiC MOSFET.

## Slide 10: Losses vs Gate Drive Voltages with 1200V M3S SiC MOSFETs
Conduction Losses highest with VGS 15V
Conduction Losses Lower with VGS 18V
25% lower
losses
EON Losses highest with VGS 15V/0V
EON Losses Losses Lower with VGS 18V/0V
25% lower
losses
EOFF Losses highest with VGS 15V/0V
EOFF Losses Losses Lower with VGS 18V/0V
3% lower
losses
EOFF Losses Losses Lowest with VGS 18V/-3V
25% lower
losses
EON Losses Losses Lowest with VGS 18V/-3V
3% lower
losses
Conclusion:
15V/0V is totally fine with onsemi
18V drive always technically better
18V/-3V drive gives the best results
Lower Rg:
Lower losses
Higher dv/dt
Higher di/dt
Lower Rg:
Lower losses
Higher dv/dt
Higher di/dt
Notes: Using 15V Turn-on gate voltage and 0V turn-off gate voltage is totally fine with all onsemi SiC MOSFETs. But, to get most out of onsemi SiC MOSFET, 18V Turn-on gate voltage saves 25% conduction losses and 25% turn-on losses (or Eon). Using negative Turn-off gate voltage saves 25% more on Turn-off losses (or Eoff). So 18V/-3V is the best combination for Gate drive voltage and gives the best results possible in the final application.
Lowering the Gate drive resistance (or Rg) lowers the losses also, but this also increases dv/dt and di/dt, and so EMI. All onsemi SiC MOSFETs have been tested to withstand dv/dt up to 50V/ns.

## Slide 11: onsemi EliteSiC Driver requirements
Gate drive voltage :
  Fast switching speed devices, up to 200V/ns on the drain
    Miller capacitor (Drain-to-Gate) can inject large current on the Gate
  Large Gate voltage amplitude : -5V to 20V
Fast dynamic performances (Delay, rise and fall time)
Embedded negative voltage bias
UVLO : 12V to 18V
Isolation helps high speed driving and breaking Ground Loop noise
Extra Protection features
  Miller Clamp
  Fast DESAT for over-current protection
  Soft Turn-off
  Over temperature protection via external sensor (Example NTC)
Notes: As SiC MOSFET is more a variable resistor as a function of the gat voltage, the device need to be driven with the maximum gate voltage possible to get the most out. So large supply voltage is required for SiC Gate drivers. As switching speed can be as high as 100V/ns, Gate Driver need to have larger dv/dt immunity. onsemi gate drive can withstand up to 200V/ns. Strong gate current capability (and clamp) is also needed because the MOSFET high speed switching injects a large amount of current in the gate via the Miller (Drain-to-Gate) parasitic capacitor. Dynamic performances should match also MOSFET dynamics, and all timing should be as short as possible. Isolation is almost a mandatory feature at such high switching speed. It avoids facing complicate ground loop problems.
Extra features available in onsemi Gate Drive can be helpful for customers and will secure the system behaviors.

## Slide 12: Portofolio
Discrete MOSFETs and Diodes

## Slide 13: Power Integrated Modules (PIM)
Product | Description | Configuration | Package
NXH006P120MNF2 | Half Bridge 2-PACK 1200V 6mΩ M1 SiC MOSFET | Press-fit pins TIM option | F2
NXH010P120MNF1 | Half Bridge 2-PACK 1200V 10mΩ M1 SiC MOSFET |  | F1
NXH020P120MNF1 | Half Bridge 2-PACK 1200V 20mΩ M1 SiC MOSFET |  | 
NXH040P120MNF1 | Half Bridge 2-PACK 1200V 40mΩ M1 SiC MOSFET |  | 
NXH010P090MNF1 | Half Bridge 2-PACK 900V 20mΩ M2 SiC MOSFET |  | 
NXH020U90MNF2 | Vienna Module 900V 10mΩ M2 SiC MOSFET & 1200V 100A D1 SiC Diode | Press-fit pins + TIM | F2
NXH020F120MNF1 | Full Bridge 4-PACK 1200V 20mΩ M1 SiC MOSFET | Press-fit pins TIM option | F1
NXH040F120MNF1 | Full Bridge 4-PACK 1200V 40mΩ M1 SiC MOSFET |  | 
NXH40B120MNQ0SNG | 2 channel Boost 1200V 40mΩ M1 SiC MOSFET, 1200V 40A D1 SiC Diode | Solder pin (S) Ni plated DBC | Q0
NXH80B120MNQ0SNG | 2 channel Boost 1200V 80mΩ M1 SiC MOSFET, 1200V 20A D1 SiC Diode |  | 
NXH40B120MNQ1SNG | 3 channel Boost 1200V 40mΩ M1 SiC MOSFET, 1200V 40A D1 SiC Diode |  | Q1
NXH100B120H3Q0 | 2 channel Boost 1200V 50A IGBT, 1200V 20A D1 SiC Diode | Solder pins (S) or Press-fit (P) TIM | Q0
NXH240B120H3Q1PG | 3 channel Boost 1200V 60A IGBT, 1200V 20A D1 SiC Diode | Press-fit (P) | Q1
Q2
F5
Q0
Q1
F1
F2

## Slide 14: 650V SiC Diodes – D1 Family
I (A) | VFM (V) | TO-247-3L Dual | TO-247-2L | TO-220-2L | TO-220FP-2L | D2PAK | DPAK | PQFN-88 | Dies
50 | 1.75 | FFSH5065A-F155 | FFSH5065A |  |  |  |  |  | PCFFS5065AF
40 |  | FFSH4065ADN | FFSH4065A |  |  |  |  |  | PCFFS4065AF
30 |  | FFSH3065ADN | FFSH3065A | FFSP3065A |  |  |  |  | PCFFS3065AF
20 |  | FFSH2065ADN | FFSH2065A | FFSP2065A | FFSPF2065A |  |  |  | 
16 |  | FFSH1665ADN | FFSH1665A | FFSP1665A |  |  |  |  | 
12 |  |  |  | FFSP1265A |  | FFSB1265A |  | FFSM1265A | 
10 |  |  | FFSH1065A | FFSP1065A | FFSPF1065A | FFSB1065A | FFSD1065A | FFSM1065A | 
8 |  |  |  | FFSP0865A | FFSPF0865A | FFSB0865A | FFSD0865A | FFSM0865A | 
6 |  |  |  | FFSP0665A | FFSPF0665A | FFSB0665A | FFSD0665A | FFSM0665A | 
4 |  |  |  | FFSP0465A |  | FFSB0465A | FFSD0465A | FFSM0465A | 
Single die device (instead of two parallel die) created as Wolfspeed drop-in replacement.
Automotive grade includes “–F085” OPN suffix

## Slide 15: 650V SiC Diodes – D2 Family
I (A) | VFM (V) | TO-247-3L Dual | TO-247-2L | TO-220-2L | TO-220-3L Dual | D2PAK | DPAK | PQFN-88
50 | 1.7 |  | FFSH5065B |  |  |  |  | 
40 |  | FFSH4065BDN |  |  | FFSP4065BDN |  |  | 
30 |  |  | FFSH3065B | FFSP3065B |  | FFSB3065B |  | 
20 |  | FFSH2065BDN | FFSH2065B | FFSP2065B | FFSP2065BDN | FFSB2065B FFSB2065BDN | FFSD2065B | FFSM2065B
10 |  |  | FFSH1065B | FFSP1065B |  | FFSB1065B | FFSD1065B | FFSM1065B
8 |  |  |  | FFSP0865B |  | FFSB0865B | FFSD0865B | FFSM0865B
6 |  |  |  | FFSP0665B |  | FFSB0665B | FFSD0665B | FFSM0665B
Automotive grade includes “–F085” OPN suffix

## Slide 16: 1200V SiC Diodes – D1 Family
I (A) | VFM (V) | TO-247-3L Dual | TO-247-2L | TO-220-2L | D2PAK | DPAK | Die
50 | 1.75 |  | FFSH50120A (16mm) |  |  |  | PCFFS50120AF
40 |  | FFSH40120ADN-F155 | FFSH40120A-F155 |  |  |  | PCFFS40120AF
30 |  | FFSH30120ADN-F155 | FFSH30120A-F155 |  |  |  | PCFFS30120AF
20 |  | FFSH20120ADN-F155 | FFSH20120A-F155 | FFSP20120A | FFSB20120A |  | PCFFS20120AF
15 |  | FFSH15120ADN-F155 | FFSH15120A-F155 | FFSP15120A |  |  | PCFFS15120AF
10 |  | FFSH10120ADN-F155 | FFSH10120A-F155 | FFSP10120A | FFSB10120A | FFSD10120A | PCFFS10120AF
8 |  |  |  | FFSP08120A |  | FFSD08120A | PCFFS08120AF
5 |  |  |  | FFSP05120A |  |  | PCFFS05120AF
Automotive grade includes “–F085” OPN suffix. Standard 20mm lead length with “-F155” suffix for TO-247.

## Slide 17: 1200V SiC Diodes – D3 Family
IF (A) | VFM (V) | TO-247-2L | TO-247-3L
50 | 1.75 | NDSH50120C NVDSH50120C | 
40 |  |  | NDSH40120CDN
20 |  | NDSH20120C NVDSH20120C | 
Automotive grade uses “NVD” Industrial grade uses “ND”. 16mm lead length for TO-247-2L

## Slide 18: 1700V SiC Diodes – D1 Family
IF (A) | VFM (V) | TO-247-2L | Die
100 | 1.75 |  | NDC100170A
25 |  | NDSH25170A | NDC25170A
10 |  | NDSH10170A | NDC10170A
Higher BV @300uA
Vin [Vac] | Makers | BV @25ºC | BV @175ºC
NDSH10170A | onsemi | 2,090 V | 2,130 V
Competitor A | Comp A | 1,950 V | 2,050 V
Competitor B | Comp B | 1,970 V | 2,015 V
Competitor C | Comp C | 1,990 V | 1,965 V
Competitor D | Comp D | 2,065 V | 2,120 V
Excellent leakage current @1700V
More Stable high voltage operation at high temperature

## Slide 19: 650V SiC MOSFETs – M2 Family
RDS(ON) (mΩ) Typical @Vgs:15V | RDS(ON) (mΩ) Typical @Vgs:18V | TO-247-3L | TO-247-4L | D2PAK-7L | TOLL | PQFN88
15 | 12 | NVHL015N065SC1 NTHL015N065SC1 | NVH4L015N065SC1 NTH4L015N065SC1 | NVBG015N065SC1 NTBG015N065SC1 |  | 
25 | 19 | NVHL025N065SC1 NTHL025N065SC1 | NVH4L025N065SC1 NTH4L025N065SC1 | NVBG025N065SC1 NTBG025N065SC1 |  | 
45 | 33 | NVHL045N065SC1 NTHL045N065SC1 | NVH4L045N065SC1 NTH4L045N065SC1 | NVBG045N065SC1 NTBG045N065SC1 | NTBL045N065SC1 | NTMT045N065SC1
60 | 44 | NVHL060N065SC1 NTHL060N065SC1 | NVH4L060N065SC1 NTH4L060N065SC1 | NVBG060N065SC1 NTBG060N065SC1 |  | 
75 | 57 | NVHL075N065SC1 NTHL075N065SC1 | NVH4L075N065SC1 NTH4L075N065SC1 | NVBG075N065SC1 |  | 
95 | 78 |  | NVH4L095N065SC1 | NVBG095N065SC1 |  | 
Automotive grade uses “NV” Industrial grade uses “NT”

## Slide 20: 900V SiC MOSFETs – M2 Family
RDS(ON) (mΩ) Typical @Vgs:15V | RDS(ON) (mΩ) Typical @Vgs:18V | TO-247-3L | TO-247-4L | D2PAK-7L
20 | 16 | NVHL020N090SC1 NTHL020N090SC1 | NVH4L020N090SC1 NTH4L020N090SC1 | NVBG020N090SC1 NTBG020N090SC1
60 | 43 | NVHL060N090SC1 NTHL060N090SC1 | NVH4L060N090SC1 NTH4L060N090SC1 | NVBG060N090SC1 NTBG060N090SC1
Automotive grade uses “NV” Industrial grade uses “NT”

## Slide 21: 1200V SiC MOSFETs – M1 Family
RDS(ON) (mΩ) Typical @Vgs:20V | TO-247-3L | TO-247-4L | D2PAK-7L | Die – Wafer and T&R
20 | NVHL020N120SC1 NTHL020N120SC1 | NVH4L020N120SC1 NTH4L020N120SC1 | NVBG020N120SC1 NTBG020N120SC1 | NVC020N120SC1 NTC020N120SC1
40 | NVHL040N120SC1 NTHL040N120SC1 | NVH4L040N120SC1 NTH4L040N120SC1 | NVBG040N120SC1 NTBG040N120SC1 | NVC040N120SC1 NTC040N120SC1
80 | NVHL080N120SC1A NTHL080N120SC1A | NVH4L080N120SC1 NTH4L080N120SC1 | NVBG080N120SC1 NTBG080N120SC1 | NVC080N120SC1 NTC080N120SC1
160 | NVHL160N120SC1 NTHL160N120SC1 | NVH4L160N120SC1 NTH4L160N120SC1 | NVBG160N120SC1 NTBG160N120SC1 | 
Automotive grade uses “NV” Industrial grade uses “NT”

## Slide 22: 1200V SiC MOSFETs – M3 Family
RDS(ON) (mΩ) Typical @Vgs:18V | TO-247-3L | TO-247-4L | D2PAK-7L | Die
13 |  |  |  | 
14 |  | NTH4L014N120M3P | NTBG014N120M3P | 
22 | NTHL022N120M3S | NTH4L022N120M3S NVH4L022N120M3S | NTBG022N120M3S NVBG022N120M3S | 
30 |  |  |  | 
40 |  | NTH4L040N120M3S NVH4L040N120M3S |  | 
70 |  |  |  | 
Automotive grade uses “NV” Industrial grade uses “NT”

## Slide 23: 1700V SiC MOSFETs – M1 Family
RDS(ON) (mΩ) Typical @Vgs:20V | TO-247-3L | TO-247-4L | D2PAK-7L
28 |  | NTH4L028N170M1 | NTBG028N170M1
1000 |  |  | NTBG1000N170M1 ( Sep ’22 / Apr ’23 )

## Slide 24: Isolated SiC Gate Drivers Single and Dual
OPN | Key Feature(s) | Package Type | UVLO (V) | TPD (ns)
Single High Speed SiC Gate Drivers for Discretes |  |  |  | 
NCP(V)51152CA/DA | Single-Channel Driver, Split Output | SOIC-8 Narrow | 12 or 17 | 45 ns
NCP(V)51152CB/DB | Single-Channel Driver, True Vcc UVLO | SOIC-8 Narrow | 12 or 17 | 45 ns
NCP(V)51153DA | Single-Channel Driver, Split Output | SOIC-8 Wide | 17 | 45 ns
NCP(V)51752Cx/Dx | Single-Channel Driver, Negative Bias | SOIC-8 Narrow | 12 or 17 | 45 ns
Single High Current SiC Gate Drivers for Modules |  |  |  | 
NCD(V)57100 | Full Featured Single-Channel IGBT Driver | SOIC-16 Wide | 12.2 to 12.8 | 60 ns
NCD(V)57101 | NCD57000 with Single Output | SOIC-16 Wide | 12.2 to 12.8 | 60 ns
NCD(V)57080 A/B/C | Single Channel Driver (Wide Body) | SOIC-8 Wide | 11.5 to 12.5 | 60 ns
NCD(V)57090 A/B/C | Single Channel Driver (Narrow Body) | SOIC-8 Narrow | 11.5 to 12.5 | 60 ns
NCD(V)57084 | Single Channel Driver (Narrow Body) | SOIC 8 Narrow | 11.5 to 12.5 | 60 ns
NCD(V)57085 | Single Channel Driver (Narrow Body) | SOIC 8 Narrow | 11.5 to 12.5 | 60 ns
Dual High Speed SiC Gate Drivers for Discretes |  |  |  | 
NCP51561C/D | Two-Channel Output Driver | SOIC-16 Wide | 13 or 17 | 36 ns
NCV51561C/D | Two-Channel Output Driver | SOIC-16 Wide | 13 or 17 | 36 ns
NCP(V)51563C/D | Two-Channel Driver with high creepage | SOIC-14 Wide | 13 or 17 | 36 ns
NCP51560CB/DB | Two-Channel Output Driver pin#7 NC | SOIC-16 Wide | 13 or 17 | 36 ns

## Slide 25: Back Up
Notes: DONE

## Slide 26
SiC Diodes
Chart: VF [V]
| 1.3900000000000001 | 1.33 | 1.42 | 1.43 | 1.51
ON (Gen2) ST ROHM IFX Cree | 85 | 117 | 82 | 88 | 86
Higher
Efficiency
Full SiC & Hybrid SiC Modules
Optimized for superior performance
Lower thermal resistance than discrete devices
Easy to mount packages to fit industry standard pinouts
SiC MOSFETs
TO247-3LD
TO247-4LD
D2PAK-7LD
1200V M3S SiC MOSFETs provide up to 20% power loss reduction in hard switching applications compared to industry leading competition
New D3 1200V SiC diode family minimizes conduction and switching losses to promote higher end application efficiency
onsemi’s wide range of SiC Products allows you to choose the power topology best fitting the size, cost and efficiency constraints of your design
Faster switching More compact end-product
Notes: SiC Portfolio Advantages:
SiC technology is robust – 100% avalanche rated
We use larger dies than industry leading competition which improves efficiency – RDS(ON) depends on temperature. By lowering the temperature with a larger die, our dies will then get a lower RDS(ON), improving efficiency and reduces heat output. The exact number depends on the proportion of switching losses to conduction losses which depends on many factors including the application. Applications like DC switches will benefit more from this than high speed switching applications.
Modules - we put capacitors in our modules which reduces the voltage overshoot during ringing. Overshoot is a pain for designers. So you can have faster switching and lower losses with same overshoot, or less overshoot with lower power.

## Slide 27: onsemi MOSFET and Diode Families
Family | Series | Optimization | 650V | 900V | 1200V | 1700V | Primary Applications
M1 | M1 | Low RDS(ON) High SCWT |  |  | ..120SC1 | ..170M1 | 
M2 | M2 | Low RDS(ON) High SCWT | ..065SC1 | ..090SC1 |  |  | 
M3 | M3S | High speed |  |  | ..120M3S |  | 
 | M3T | Low RDS(ON) High SCWT |  |  | ..120M3x SCWT dependent |  | 
Family | Optimization | 650V |  | 1200V | 1700V | Primary Applications
D1 | High IFSM | ..65A |  | ..120A | ..170A | 
D2 | Low QC | ..65B |  |  |  | 
D3 | Low QC x VF |  |  | ..120C |  | 
Traction
On-board Charger
EV Charging Station
UPS/Energy Storage
Solar
High Power Industrial

## Slide 28: Industrial power solutions target market & products Discrete
UPS
Servo
HVAC
Industrial Power solution
Increasing sustainability
Carbon free communities/countries
Vehicle electrification
Industry Automation
Urbanization
Increased Efficiencies
Si IGBT / Diode Discrete
  1200V FS7 IGBT
  650V FS4 IGBT
IGBT / Hybrid PIM (Power Integrated Module)
  Q0/Q1/Q2
  F1/F2/F5
  Boost / inverter / xNPC
SiC MOSFET / Diode *IPS BU support >650V
  1200V 900V M1 FET
  1200V D1/D2 Diode
  1200V M3 FET
  1700V/2300V M1 FET
Full SiC PIM
  F1/F2 2,4,6-PACK
  Pin-compatible w/ IFX, Wolfspeed
IPM (Intelligent Power module)
  1200V/650V DIP solution
  650V SIP Solution
TMPIM (Transfer Mold PIM)
  FS7 1200V IGBT
  CI/CIB/6pack
Wafer sales
Si IGBT / Diode
SiC FET / Diode