## Slide 1: Industrial HART Protocol Modems
Overview
July 2022

## Slide 2: HART protocol and applications
Smart metering, streetlight control, in-home displays, building automation, solar power
HART protocol
HART (highway addressable remote transducer) is a hybrid protocol, combining analog and digital communication over a single pair of wires
HART technology
HART communicates a single control variable to devices, using a 4-20mA analog signal at Bell 202 shift frequencies of 1200Hz & 2200Hz
HART technology
Additional information (e.g. device status, process variables) is contained in a low-level digital modulation superimposed on the standard 4-to-20mA current loop
HART communication
Transmission of additional information allows HART devices to communicate failure conditions to the host before they cause a major process problem
HART applications
Process industry automation: oil & gas, refineries, pharmaceutical, chemical, pulp & paper, food & beverage

## Slide 3: onsemi HART product family
Integrated HART transceivers for use as slave or master in twisted pair HART networks
Feature | A5191HRT | NCN5192 | NCN5193
Supply range | 3.0 V – 5.5 V | 3.0 V – 5.5 V | 1.8 V – 3.5 V
Clock speed | 60.8 kHz | 1.8432 MHz or 460.8 kHz | 3.6864 MHz
Embedded PA | - | - | Y
Integrated watchdog | - | Y | Y
Integrated POR | - | Y | Y
Integrated DAC | - | Y | Y
Digital communication | UART | UART (data)+ SPI (reconfig) | UART (data)+ SPI (reconfig)
Package | LQFP 32, QFN 32, PLCC 28 | QFN 32 | QFN 32
Ordering information | www.onsemi.com/A5191HRT | www.onsemi.com/NCN5192 | www.onsemi.com/NCN5193
Traditional
Analog control Signal
ONE Analog Variable
OR
Host
Valve (Rx)
HART Communication (1 wire pair)
Digital status (multiple), analog control signal
Host
Valve (Tx / Rx)

## Slide 4: onsemi HART modem features and benefits
Typical Application Schematic
Additional features & benefits
Unique features & benefits
Single-chip modem family for use in Highway Addressable Remote Transducer (HART) field instruments and masters
  Industrial temperature range: -40 ºC to +85 ºC
  Add-on to standard 4-20 mA communication bus
  3 to 5V power supply range (NCN5193)
  Compatible with 3.3 or 5V microcontrollers (NCN5193)
  Transmit-signal wave shaping
  Receive bandpass filter
  Meets HART physical layer requirements
  Half-duplex 1200 baud FSK modem
  Bell 202 shift frequencies of 1200 and 2200 Hz
  Several variants available:
    A5191HRT – De facto standard for HART modem
    NCN5192 – Integrated 16 bit Sigma-Delta DAC
    NCN5193 – Low power – optimal for intrinsically safe applications