## Slide 1: Isolated DC-DC Solutions
PCS BU, MCC, ASG
April. 2022

## Slide 2: Isolated DC-DC Flyback Controllers Roadmap
Existing
2022 +
Power Level
NCP12700 – 9-160 V
Current Mode Flyback Controller
MSOP-10/WQFN10
NCV/P12711 – 4-45 V
Current Mode Flyback Controller, 50 V transient
MSOP-10/DFNW-10
Existing
Developing
NCV/NCP1362 – QR PSR Flyback
No opto, CC.CV with BO. Target Auto AUX
Sampling, RTM Q2’22
NCP1568D AC Flyback
NCP1568 option for DC-DC & POE Applications, TSSOP-18
Samples Available
NCP1566 120V AC Forward
Enhanced Active Clamp Forward Controller
Current & Voltage Ctrl– QFN24
NCL30125 – 2-SW Forward
Enhanced Forward Controller with HB drivers , Current & Voltage Ctrl– QFN24
*AEC-Q100 version
Exploring

## Slide 3: NCP12700 – 9 V to 160 V Flyback Controller
Industrial
Telecom
Transportation
Suitable for 2:1, 4:1, 8:1 input range designs
The NCP12700 is a wide-input range, fixed frequency, peak current mode PWM controller with a highly integrated feature set suitable for implementing single-ended power converter topologies.
Ultra Wide Range HV (9 – 200 V) startup regulator
User Adjustable Over-Power Protection
Fault pin for thermal and
output over-voltage protection
Eliminate external startup components
Easier design across input voltage range
Interface for thermal and output OVP eliminates external protection
NCP12700xDMR2G in Micro10 3*3 (9-100 V)
NCP12700xMNTWG in WQFN10 3*4 (9-200 V
Programmable oscillator: 100 kHz – 1 MHz
Internal slope compensation
Adjustable Soft-Start Ramp
Input Voltage UVLO with hysteresis
Shutdown Threshold for External Disable
Overload Protection with 30 ms Overload Timer
1 A / 2.5 A Source / Sink Gate Driver
Other Features
Market & Applications
Ordering & Package information
Value Proposition
Unique Features
Unique Features
Typical Application Schematic & Pin Out

## Slide 4: NCP12700 9 – 36 V Input Demoboard
4:1 Input Voltage Range: 9 – 36 V
Output: 12 V/1.25 A, 15 W
Full Load Efficiency: > 88 % / 91% peak
Startup time: < 30 ms
Transient Response: < 250 µs
No Load Output Ripple: 200 mVpp Max
No Load Power: 120 mW Max
Overvoltage Protection: 16 VDC Max
DC/DC Power
DC/DC Modules
Market & Applications
Specifications and Features
Demo Board Photo
Design Note
OPN: NCP12700LOWVINGEVB

## Slide 5: NCP12700 18 – 160 V Input Demoboard
9:1 Input Voltage Range: 18 – 160 V
Output: 12 V/1.25 A, 15 W
Full Load Efficiency: > 86 % / 90% peak
Startup time: < 20 ms
Transient Response: < 250 µs
No Load Output Ripple: 150 mVpp Max
No Load Power: 500 mW Max
Overvoltage Protection: 16 VDC Max
DC/DC Modules
Telecom
Power Over Ethernet
Market & Applications
Specifications and Features
Demo Board Photo
Design Note
OPN: NCP12700WIDEVINGEVB

## Slide 6: NCP12700 45 W, 24 V Power over Ethernet PD Demo Board
Power Over Ethernet Compatible Input Range: 37 V to 57 V
High Full Load Efficiency: >90%
and Average Efficiency
Very Low Ripple and Noise
Smooth Startup Operation
Low Parts Count
Inherent SCP And OCP Protection
Thermal and OVP Protection
Multiple Probe Points for Evaluation
Compatible with the NCP1096GEVB
Power Over Ethernet
Market & Applications
Specifications and Features
Demo Board Photo
Design Note
Connected to the NCP1096GEVB POE PD Demo

## Slide 7: NCP12700 45 W POE TO USB PD Demo
Power Over Ethernet Compatible Input Range:37 V to 57 V
USB−PD 5V−20V Operation
High Full Load and Average Efficiency
Very Low Ripple and Noise
Smooth Startup Operation
Low Parts Count
Inherent SCP And OCP Protection
Thermal and OVP Protection
Multiple Probe Points for Evaluation
Compatible with the NCP1096GEVB
Power Over Ethernet to USB PD
Market & Applications
Specifications and Features
Demo Board Photo
Design Note
Connected to the NCP1096GEVB POE PD Demo

## Slide 8: NCP1566 Active Clamp Forward Controller
24 V & 48 V Telecom Systems
Server Power Supplies
48 V Automotive Applications
The NCP1566 is a highly integrated dual-mode active-clamp PWM controller to implement an isolated active clamp forward or asymmetric half-bridge converter. It which can be configured in either voltage mode control with input voltage feed-forward or peak current mode control. Peak current mode control may be implemented with input voltage feedforward as well.
Voltage Mode & Current Mode Control
Line feedforward
Adaptive Overlap Time Control
Integrated 120 V HV Startup
Flexible Topology Solution
Stable Constant Crossover Across Input Voltage Range
Extended ZVS Across Input & Output
Lossless Startup & Reduced Vcc Capacitor
NCP1566MNTXG in QFN-24
Vcc: 6.5 V to 20 V
Programmable UVLO
Cycle by Cycle Peak Current Limiting
Adjustable Over Power Production & Overcurrent Protection
Programmable Duty Ratio Clamp
Programmable Oscillator with 1-MHz Max Frequency & Synchronization Pin
Main Switch Drive: -2 A/3 A, Active Clamp Drive: -2 A/1 A
Other Features
Market & Applications
Ordering & Package information
Value Proposition
Unique Features
Unique Features
Typical Application Schematic & Pin Out

## Slide 9: NCP1566 3.3-V/30-A Demoboard for Telecom
This design is based around active-clamp forward converter operated in current-mode control. This controller offers many features to build an energy efficient converter with all the needed protections like cycle-by-cycle current limit with a 500-mV sense voltage, over current protection (OPP) for a stable maximum output current limit, over temperature protection with a dedicated NTC pin and a pin to sense an output voltage runaway (loop failure for instance).
36-72 V dc input
3.3-V/30-A output
>90% efficiency
Internal 120-V start-up source operated in dynamic self-supply during start-up or skip mode.
Voltage- or current-mode control operation
Adaptive dead time for improved efficiency
Line compensation for over power protection
Maximum V-s limit and duty ratio clamp
Short circuit protection
Over voltage protection
5-V/2% voltage reference
Over temperature protection via an NTC
Fault reporting pin also used for shutdown
Synchronization capability via dedicated pin
Value Proposition
Demo Board Photo
Key Features
OPN: NCP1566TELECGEVB

## Slide 10: NCP1566 5-V/10-A Active Clamp Foward Demo Board
This design is based around active-clamp forward converter operated in current-mode control. This controller offers many features to build an energy efficient converter with all the needed protections like cycle-by-cycle current limit with a 500-mV sense voltage, over current protection (OPP) for a stable maximum output current limit, over temperature protection with a dedicated NTC pin and a pin to sense an output voltage runaway (loop failure for instance).
Internal 120-V start-up source operated in dynamic self-supply during start-up or skip mode.
Voltage- or current-mode control operation
Adaptive dead time for improved efficiency
Line compensation for over power protection
Maximum V-s limit and duty ratio clamp
Short circuit protection
Over voltage protection
5-V/2% voltage reference
Over temperature protection via an NTC
Fault reporting pin also used for shutdown
Synchronization capability via dedicated pin
Value Proposition
Demo Board Photo
Key Features
OPN: NCP1566TEL5V10AGEVB
Design Note

## Slide 11: 12-V/6-A for Power over Ethernet Demo Board
This design is based around active-clamp forward converter operated in current-mode control. This controller offers many features to build an energy efficient converter with all the needed protections like cycle-by-cycle current limit with a 500-mV sense voltage, over current protection (OPP) for a stable maximum output current limit, over temperature protection with a dedicated NTC pin and a pin to sense an output voltage runaway (loop failure for instance).
Internal 120-V start-up source operated in dynamic self-supply during start-up or skip mode.
Voltage- or current-mode control operation
Adaptive dead time for improved efficiency
Line compensation for over power protection
Maximum V-s limit and duty ratio clamp
Short circuit protection
Over voltage protection
5-V/2% voltage reference
Over temperature protection via an NTC
Fault reporting pin also used for shutdown
Synchronization capability via dedicated pin
Value Proposition
Demo Board Photo
Key Features
OPN: NCP1566POE12V6AGEVB
Design Note

## Slide 12: NCP/NCV1362: Primary Side PWM Controller
AC/DC Adapters and Power
Industrial Auxiliary Power
Automotive Auxiliary Power
The NCV/NCP1362 is a new quasi−resonant peak current mode control mode controller targeting output power levels from a few watts up to 50 W in a flyback application. It is primary side regulated for Constant Voltage and Constant Current regulation, achieving excellent line and load regulation of 5% without requiring the typical opto-coupler and voltage reference for lower cost and improved system reliability. The controller features improved light load efficiency and stand-by performance.
Dual Frozen Peak Current
Constant Voltage & Current PSR < ±5%
AEC-Q100 Qualified (NCV1362)
Optimize Light Load Efficiency and Standby
Regulated Output without Opto-Coupler
Automotive Applications
Standard Part #: NCP1362
Package: SOIC-8
AEC-Q100: NCV1362
Quasi-Resonant with Valley Lockout
Max Frequency Clamp (80, 110, 140 kHz and no Clamp)
Frequency Jittering
LFF and BO on Dedicated Pin
Other Features
Market & Applications
Ordering & Package information
Value Proposition
Unique Features
Unique Features
Typical Application Schematic & Pin Out

## Slide 13: New Product NCP12711

## Slide 14: NCP12711 Low Vin DC-DC Flyback Controller
DC-DC Converters for Modules and Telecom Application
Industrial Power
Automotive 12 V Auxiliary Power Supply
The NCP12711 is a fixed-frequency peak-current-mode PWM controller containing all of the features necessary for implementing single-ended power converter topologies. The device operates from 4 V to 45 V without auxiliary winding.
Low Voltage Operation
Adjustable Over Power Protection
NTC-Compatible Fault Interface
Frequency Jitter
Error Amplifier Option
AEC-Q100 Qualified (NCV12711)
4 – 45 V Input Range
Limits Total Power Capability
Provides Thermal Protection
Improves EMI signature
For non-isolated designs
For automotive applications
Other Features
Market & Applications
Ordering & Package information
Value Proposition
Unique Features
Unique Features
Typical Application Schematic & Pin Out
Sampling, RTM Q2’22
Internal 7.5-V Regulator
0% Duty Ratio Operation in No-Load Condition
Single Resistor Programmable Oscillator – 100 kHz to 1 MHz
Adjustable Soft-Start on Peak Current and Frequency
Output OVP Fault Interface
± 1 A Source / Sink Gate Driver
NCP12711ADNR2G, MSOP-10
AEC-Q100: NCV12711

## Slide 15: NCP12711 Pin-out
Pin Name | Pin description
UVLO | Input voltage UVLO and external disable/enable interface Input voltage detection for over-power compensation
FB | FB pin to connect the voltage divider observing the regulated variable
VIN | Connects to the input rail and supplies the IC via a Low voltage dropout (LDO)
RT | Timing resistor for setting of switching frequency
COMP | Op-amp output to which the compensation network connects
SS | Connect a capacitor for setting soft-start duration in both peak current and frequency
CS | Current sense Slope compensation adjustment via a series resistance
GND | IC GND
DRV | Output driver for power switching FET clamped to 10 V.
VCC | Input pin to supply the controller

## Slide 16: NCP12711 - Isolated and PSR-type of Converters
Non-isolated primary-side regulation
Isolated primary-side regulation
The NPV12711 includes an op-amp and allows for direction connection to Vout
It can also be used in a classical auxiliary-winding-based regulation for raw dc output regulation

## Slide 17: Comparative Performance
 | ON NCP12711 | ON NCP12700 | TPS40210(-Q1) | LM5155-Q1 | Benefits
Topology | Iso. Flyback Non-Iso Flyback | Iso. Flyback | Boost/SEPIC Non-Iso Flyback | Boost/SEPIC/ Non-Iso Flyback | Optimized for isolated flyback
Input Voltage Range | 4 – 45 V | 9 - 100 V (MSOP10) 9 – 200 V (WQFN10) | 4.5 – 52 V | 3.5 – 45 V 2.97 – 16 V BIAS=Vcc | 4 V required for modules
Switching Frequency | 100 kHz to 1 MHz | 100 kHz to 1 MHz | 35 kHz to 1 MHz | 100 kHz to 2.2 MHz | 
Soft Start | Adjustable | Adjustable | Adjustable | Adjustable | 
Current Sense Threshold | 250 mV | 250/495 mV | 150 mV | 100 mV | 
Programmable Oscillator | Yes | Yes | Yes | Yes | 
Max duty ratio | 90% | 80% | - | 93% | 
tON(min) (typical) | 125 ns | 125 ns | 275 ns @ 12 V | 50 ns | 
Jitter | Optional | No | No | No | Facilitates EMI
0% duty ratio | Yes | Yes | No | No | Safe no-load operation in low-power isolated converters.
External Sync | No | No | Yes | Yes | Sync to external clock
Faults | OCP, OPP, SCP, UVLO | OCP, OPP, PTP/OVP (FLT), SCP, UVLO | OCP, UVLO | OVP, SCP, Thermal Shutdown, UVLO | Fewer external components, robustness
Auto-recovery | Auto-Recovery/Latch | Auto-Recovery/Latch | OCP Retry | - | Design flexibility
ESD, HBM | 2 kV | 2 kV | 2 kV | 2 kV | 
Operating Junction Temp | -40 °C to +125 °C | -40 °C to +150 °C | -40 °C to +125 °C | -40 °C to +125 °C | Characterization up to 150 °C
Packages | MSOP10 | MSOP10 WQFN10 | HVSSOP10, VSON10, PDSO10 | 3x2 WSON12 (wettable flank) | Leadless with wettable flanks for inspection

## Slide 18: NCP12711 in Details

## Slide 19: Overview
Peak-current-mode control with adjustable slope compensation
Adjustable fixed-frequency 100 kHz to 1-MHz operation
Optional internal frequency jitter
Guaranteed startup for Vin = 4 V up to Vin = 45 V continuously
Guaranteed operation after startup down to Vin = 3.7 V
Internal 7.5-V Vcc regulator – direct connection to Vin up to 30 V
Junction temperature of 125 °C max and characterization data up to 150 °C
Internal over-power protection
OTP/OVP via a multi-function pin
250-mV maximum peak current setpoint
Adjustable soft start in peak current and frequency
90% (typ) max duty ratio limit and 0% operation
Standby mode via UVLO pin
30-ms overload timer with 1-s auto-recovery time
Options for 100 and 200-ms durations

## Slide 20: Soft Switching Frequency Increase at Power Up or in Fault
Most controllers start switching at maximum frequency
NCP12711 switches at 30 kHz and increases frequency during the SS sequence
Overall stress is minimized, especially with a secondary-side sync rectifier
Power up
Fsw
Fsw
t
30 kHz
5 ms
Tsw
30 kHz

## Slide 21: Smooth Secondary-Side Current
Secondary-side stress is also reduced. Here, a high-line start-up sequence.

## Slide 22: Adjustable Compensation Ramp
Vdd
ton
To PWM
CS
Adjust compensation level
Rramp
Select the exact amount of slope compensation in relationship to Lp
Avoid peak power limitation at low line inherent to internal compensation ramp
Implemented in numerous controllers
Compensation ramp is needed for CCM operation and D > 50%

## Slide 23: OverPower Protection - OPP
A converter can deliver more power in high-line conditions
The stress on the switching components increases
Precautions are needed to keep away from failure
4-40 V, 5 V/1 A flyback converter
6.3 W
4 V
11.3 W
Lp = 1.5 µH
Fsw = 250 kHz
Rsense = 40 mΩ
Iout,LL = 1.3 A
Iout,HL = 2.3 A
OPP is needed

## Slide 24: Internal Peak Reduction
Maximum peak current decrease relies on the UVLO pin
A scaled version of Vin is sensed and affects VCS(max)
A 20% reduction in VCS(max)
6.3 W
4 V
7.2 W
Without OPP
With OPP
OPP keeps the maximum current under 1.5 A for a 1-A nom. value

## Slide 25: Fault Input for OVP and OTP
You can accurately shut the converter off in overheat conditions
Adding an extra winding and a Zener diode ensure a rugged OVP
VCC from auxiliary winding
Precisely-monitored
operating temperature
Build rugged converters with this 2-function pin

## Slide 26: System Performance

## Slide 27: Evaluation Board – NCV12711 with SSR Regulation
This board is designed to deliver 12 V/1 A from a 4.5- to 45-V input voltage
Its main purpose is to let the designer test the part along its full operating range

## Slide 28: Demonstration Board – NCV12711 with PSR regulation
This board is designed to deliver 12 V/1 A from 4.5 to 45 V
Main application is an automotive converter without optocoupler
The auxiliary winding is used for a simple yet efficient regulation means

## Slide 29: Waveforms
Design note will be available soon

## Slide 30: Demonstration Board – NCV12711 Floating PSR
This board is designed to deliver 12 V/1 A from 4.5 to 38 V
Main application is an automotive converter without optocoupler & auxiliary winding.
The MOSFET is floating like a buck converter.

## Slide 31: Waveforms
Design note will be available soon

## Slide 32: SIMPLIS® Models are Ready
SIMPLIS® application circuit
NCV12711

## Slide 33: A Smooth Start-Up Sequence
Vin = 4 V – LDO is off
Vin = 10 V – LDO is active
Fsw = 30 kHz
Fsw = 120 kHz

## Slide 34: Frequency Response is also Available
Loop gain, Vin = 4 V
fc = 700 Hz, m = 73°
Loop gain, Vin = 36 V
fc = 1.2 kHz, m = 80°

## Slide 35: A CADENCE’s PSpice® Model is Available