## Slide 1: KNX Arduino Shield Evaluation Boards
May 2022
Mike Sandyck

## Slide 2: KNX Network and Applications
KNX.org - The world’s most adopted standard for building automation
  KNX.org celebrated it’s 30th birthday in 2019, counts 495 members, 8000 certified products, 490 training centres, 90.000 installation partners across 190 countries
KNX is an intelligent control system standard through which all applications and devices in a building automation system can communicate
The major advantage is the multi-vendor interoperability through certification and training centers for installers
  The KNX network allows for up to 256 devices along one 1000m segment, and up to 256 segments in a network
Worldwide Standard
Applications
Network
The communication bus is separated from the actuator power delivery, and can consist of different forms of physical layer (Twisted Pair, IP, RF, Power Line Comms, …)
Typically used is Twisted Pair, that performs a double function: supply enough power for the sensor or switch, and allowing communication at a data rate of 9,6kbps
Technology

## Slide 3: Arduino Shield Evaluation Board Features
Arduino Uno V3 connections compatible with a wide variety of microcontroller boards
Fully TP-UART compatible
Enhanced KNX Transceiver to MCU communication diagnostics
Selectable fan-in:
  Up to 40mA on the NCN5130 version
  The NCN5121 goes up to 24mA
Two high efficiency DC-DC converters
  3.3 V fixed
  1.2 to 21 V selectable
Integrated 20 V linear regulator

## Slide 4: NCN51xxASGEVB – Major components
KNX Line In
Transmit Resistor
Protection Diodes
NCN5130 Transceiver
Arduino Uno V3 Shield connector
Arduino Uno V3 Shield connector
4x Pushbutton + LED
GND
DCDC2 9V LDO 20V Output
Baud Rate Jumpers
Buffer Cap
NCN5130ASGEVB
DCDC Coils
Generic XTAL 16MHz
Transceiver Area < 2x2 cm²

## Slide 5: Smallest Footprint Solutions & Lowest BoM Cost
Only 17 components + IC (DCDC1 and XTAL populated)
Small buffer cap (down to 27µF)
Low cost 16MHz crystal
MCU clock out
Integrated DC-DC convertors (NCN5110/21/30)
LDO (NCN5121/30)
NCN5121/5130 MAC + PHY Transceivers

## Slide 6: Example Bit Transceiver with minimal footprint
Before Competition solution, on 4-layer PCB
After
NCN5110 based PCB
Lower BOM
Single sided assembly possible
2-layer PCB
NCN5110 Bit Transceiver

## Slide 7: Support and Collateral
User Manual
User Manual
Datasheets
NCN5130 NCN5121
NCN5110
App Note
LC Selection Guide
Design Tools
Efficiency Calculator
* Live weblinks in the headers *

## Slide 8: Key Product Information
Devices: NCN5110, NCN5121, NCN5130 Evaluation Boards: NCN51xxASGEVB

## Slide 9: KNX Twisted Pair Modems and Transceivers
Certified KNX transceiver for use in twisted pair networks
  Certified KNX transceivers
  Two DC-DC converters; 3.3V fixed, 1.2 to 21V selectable
  Low voltage drop for increased efficiency
  Supervision of KNX bus voltage and current
  Supports bus current consumption up to 40mA
  Enhanced transceiver to mcu communication diagnostics
  Lower BOM cost
  Temperature monitoring
  Linear 20V regulator output
  Certified software stacks through Weinzierl and Tapko
  Extended temperature range: -40 to 105°C
  Building Control and Automation
  Security and Monitoring
  Lighting Control
  IP Connectivity and Remote Access
  QFN40 6x6
  NCN5110: Analog PHY
  NCN5121, NCN5130: PHY + MAC
  http://www.onsemi.com/PowerSolutions/product.do?id=NCN5130
Unique Features & Benefits
Other Features & Specifications
Markets & Applications
Typical Application Schematic
Ordering & Package Information

## Slide 10: Existing Family Portfolio
 | NCN5110 | NCN5121 | NCN5130
Implements | PHY | MAC+PHY | MAC+PHY
Analog monitoring of Vbus, Vfilt, DC2, DC1, V20V, Ibus, Temp | No | Yes | Yes
Analog fan-in model (5-40 mA) | Yes | No | Yes
Requires crystal | No | Yes | Yes
Communication interface | Analog | UART/SPI | UART/SPI
DCDC Convertor 3.3V fixed | Yes | Yes | Yes
DCDC Convertor 1.2 to 21V adjustable | Yes | Yes | Yes
LDO 20V adjustable current limit | No | Yes | Yes
EVB Order Code | NCN5110ASGEVB | NCN5121ASGEVB | NCN5130ASGEVB

## Slide 11: Industry leading KNX Transceivers
High degree of integration, Low BOM cost, compact design size
  DCDC1 (3.3V fixed @ 100mA)
  DCDC2 (1.2 – 21V @ 100mA), additional, adjustable DCDC convertor
  20V LDO
  MCU clock out frequency (8 or 16MHz)
Industry leading efficiency
  High system efficiency: Low bus current draw, Low bus voltage drop
  High efficiency of onboard DCDC convertors (%%%)
High system reliability / robust communication
  Diagnostic features on MCU/MAC communication
  Extensive system & bus signal monitoring options (Vbus, Vfilt, DC2, DC1, V20V, Ibus, Temp)
  Support for TPUART communication and TP1-256 (256 max devices per line)
Additional benefits:
  High max current draw from the bus (up to 40mA)
  Very fast start-up time
  Extended operating temperature range -40° ~ +125°C
onsemi key benefits
A++
A+
A
B
C
5/25/2022
11

## Slide 12: Additional Supporting Data
KNX Secure
Notes: Plots, charts, graphs, and any additional data that supports previous slides.

## Slide 13: KNX Secure
The latest addition to the standard is KNX Secure, lifting the platform to new levels of automation security. KNX Secure is implemented into two layers.
KNX Data Security prevents data manipulation, by encrypting all the data that is sent around the network.
Up to 256bit AES encryption can be used to ensure a high level of protection.
Frame format that is unchanged, so secure messages can be routed through existing network
Existing couplers and devices will not be hampered by this new secure communication.
Meaning new secure nodes can be dropped into existing networks without interoperability issues, and be implemented on any physical layer (= including Twisted Pair with ON KNX Transceivers)
KNX IP Secure protects the setup from unauthorized access. In other words no-one without proper access can manipulate the settings of the devices and the network. This can only be used on IP links and is therefor only used on the backbone IP links of the network.