## Slide 1: NCL31000/1
Intelligent LED Driver
June 2021
Notes: *Mandatory Slide*
Above information can be pulled from onsemi.com if needed.

## Slide 2: NCL31000/1 - Intelligent LED Driver
Multi-Channel Example
Product Family Overview
Applications
Smart LED Lighting
  Energy saving lighting Systems
  Human Centric Lighting
  Communication Lighting
IoT Home appliances
Input Voltage from 35V to 57V
97% efficient Buck Controller LED driver
Integrated 3V3 Buck Converter (150mA) for companion MCU.
Integrated Adjustable Buck Converter 2.5-24V
SPI or I2C interface for RF connectivity
Active Fault protection and diagnosis for LED shorts/opens,..
  Over/Under Voltage, Over Current, LED Temperature
Visual Light Communication capable, Yellow-Dot ready, up to 10kb/s
Linear, high bandwidth dimming to zero (full range linearity 0.05% INL)
Deep dimming down to 1mA or 0.033% @3A full scale current
Digital Dimming over I2C/SPI (Warm Boot)
High accuracy diagnostic functions to measure voltages/currents
Junction temperature range of -40°C to +125°C
Available in 48-pin QFN 7x7
NCL31001 enables multi-channel operation
System Block Diagram

## Slide 3: NCL3100x VLC Family Summary
Integrated DCDC’s
DCDC’s removed for Multi Channel Applications
NCL31000:
NCL31001:
Production/ON Target
Production/ON Target
NCL31000 Family Key Features
Power Supply
High Input Voltage (24 ~ 57V)
Integrated 3.3V Buck (NCL31000 only)
Adjustable 2.5-24V Buck (NCL31000 only)
Accurate Voltage (2.4V+/-0.3%)
Buck LED Driver
Linearity (full range) 0.05% INL
Deep Dimming to 1mA = 0.066% of 1.5A or 0.033% of 3A
Efficiency (97%)
Spread Spectrum PWM
Connectivity
Serial Interface SPI or I2C
Protections/Diagnostics - LED Temperature, Over/Under Voltage and Over Current
Power Metrology Accuracy (1%)
Part Number | Integrated DCDC1 DCDC2 | I2C | SPI | Adjustable UVLO
NCL31000MNIYWG | ✓ | ✓ |  | >100W LED Driver
NCL310000MNSTWG | ✓ |  | ✓ | >100W LED Driver
NCL31001MNITWG |  | ✓ |  | Multi Channel Enabler
NCL31001MNSTWG |  |  | ✓ | Multi Channel Enabler

## Slide 4: What is YellowDot?
YellowDot is an indoor position location technology
Each LED ballast has a unique identifier that indicates the position within a building
LED ballast signals through visible light communication (VLC) to a camera on a phone or tablet
Phone’s camera detects the code and reveals the position
Accuracy to within 30cm; BLE accuracy is 3 meters
Certification requires a range of tests; passing allows the use of the YellowDot trademark to a luminaire
Has two defined data rates: 1kb/s and 2kb/s

## Slide 5
Data Sheets
Click Here
Product Page URL
Click Here
Videos
Click Here
Evaluation Boards
NCL31000ASGEVB
Collateral
Pricing
  NCL31000ASGEVB: $65
    MPQ: 1
    Evaluation Board
  NCL31001MNITWG: $3.42
  NCL31001MNSTWG: $3.42
  NCL31000MNITWG: $3.64
  NCL31000MNSTWG: $3.64
    MPQ: 2,500
    QFN-48
Data Sheets
Click Here
Product Page URL
Click Here
Blog
Click Here
Press Release
Click Here
NCL31000
NCL31001