## Slide 1: NCP11184,NCP11185,NCP11187
800V HV AC-DC Switcher, 7DIP
December, 2021
Notes: *Mandatory Slide*
Above information can be pulled from onsemi.com if needed.

## Slide 2: NCP1118x – 800 V HV AC-DC Switcher
Value Proposition
Product Family Overview
Applications
Features
Internal rugged 800 V MOSFET and Built-in HV current source for start up
- NCP11184: 2.25 Ω(Max.)
- NCP11185: 1.3 Ω(Max.)
- NCP11187: 0.87 Ω(Max.)
mWSaverTM Technology and Frequency Foldback
Variable FSW option: 65/100/130 kHz
Line compensation for constant maximum over load limiting
Various Protections; AR or Latch
Industrial
  Motor Inverter Aux Power
  Adapter Power supply (<50 W)
Consumer
  White goods Aux Power
  IoT terminals Power supply
  Adapter Power supply (<50 W)
The NCP1118x series integrates a peak current mode PWM controller employing mWSaver™ technology and a highly robust 800 V Super Junction MOSFET providing especially enhanced performance in 30 ~ 50 W Flyback converters.
Easy and Rugged design with minimal external component
Low standby power; <25 mW
Allows design trade-off between space and efficiency
Design flexibility
High system reliability
System or Application Block Diagram

## Slide 3
Existing Product Portfolio & Competitive Comparison

## Slide 4
NCP1118x Selection Guide
Part Number | Package | Switching Frequency | Max. RDS(ON) [Ω] | Output Power Table [W] | 
 |  |  |  | Open Frame | 
 |  |  |  | 85 ~ 265 VAC | 230 VAC
NCP11184A065PG | PDIP-7 | 65 kHz | 2.25 | 35 | 45
NCP11185A065PG |  |  | 1.3 | 40 | 55
NCP11187A065PG |  |  | 0.87 | 50 | 65
NCP11184A100PG |  | 100 kHz | 2.25 | 33 | 40
NCP11187A100PG |  |  | 0.87 | 45 | 60
NCP11184A130PG |  | 130 kHz | 2.25 | 30 | 36
NCP11185A130PG |  |  | 1.3 | 37 | 52

## Slide 5
Data Sheets
Click Here
Simulation Model
Simplis Model
Design Tool
Excel calculator
Evaluation Boards
NCP11184A65P25WGEVB
NCP11185A130P38WGEVB
NCP11187A65P45WGEVB
Collateral
Pricing
  NCP11184A065PG, NCP11184A100PG, NCP11184A130PG: $0.708
    3000
    PDIP-7
  NCP11185A065PG, NCP11185A130PG: $0.772
    3000
    PDIP-7
  NCP11187A065PG, NCP11187A100PG: $0.961
    3000
    PDIP-7