## Slide 1: NCP1343
Quasi-Resonant Flyback Controller with Power Excursion Mode July 2021
Notes: *Mandatory Slide*
Above information can be pulled from onsemi.com if needed.

## Slide 2: NCP1343 Quasi-Resonant Flyback Controller
Product Family Overview
Applications
Features
Valley Switching Operation with Valley Lockout
New Quiet-Skip Technology
Min Peak Current Modulation for Rapid Frequency Foldback (RFF)
Power Excursion Mode (PEM) (NCP1343)
High voltage startup circuit with Integrated Brownout
Valley Switching Operation with Valley Lockout
Frequency Foldback with 25 kHz Minimum Frequency
VCC Overvoltage Detection
NTC Compatible Fault Pin
Soft-Start for Smooth Start-up Operation
High Drive Capability: -500 mA / +800 mA
Benefits
Maximizes the efficiency over the entire power range
Ensures Operation Outside Audible Range
Fast reduction of switching frequency for improved light load efficiency
Minimize transformer size for peak power applications
Audio Power
Notebook Adapters
Medium or High Power AC-DC Adapters
Ultra High Density AC-DC Adapters
Flat TV SMPS
Computer Power Supplies
Phone and Tablet Adapters
Typical Application Schematic
The NCP1342/3 is a highly integrated quasi-resonant flyback controller capable of controlling rugged and high-performance off-line power supplies as required by adapter applications. Additionally, the NCP1343 integrates power excursion mode (PEM) to minimize transformer size in designs requiring high transient load capability

## Slide 3: Existing Family Portfolio & Internal Positioning
The NCP1343 upgrades the NCP1341 with the additional of Minimum Peak Current Modulation for Rapid Frequency Fold-back (RFF) and additional configuration options, allowing designs to be better optimized. They are pin-to-pin compatible.
Feature | NCP1340 & NCP1341 | NCP1342 & NCP1343 | Comments
Power Excursion Mode (PEM) | NCP1341 | NCP1343 | 
HV Start-Up | Yes | Yes | 
X2 Discharge | Yes | NCP1342 | 
Integrated BO in HV Pin, VCC OVP | Yes | Yes | 
NTC Compatible Fault Pin | Yes | Yes | 
6 Valley Operation, Frequency Foldback | Yes | Yes | 
Improved Linear Dead-Time | Yes | Yes | Reduces power consumption at light loads
Rapid Frequency Foldback | No | Yes | Fast reduction of fsw at light loads for improved performance
Minimum Dead-Time Added | 0 µs | 0 µs | Allows higher fsw
25 kHz Min Freq | Yes | Yes | 
Quiet-Skip | Yes | Yes | Avoids the audible frequency range
Adjustable OPP | Yes | Yes | 
FMAX Clamp | Fixed/Adjustable/None | Adjustable/None | 
Jitter | Yes | Yes | Jitter on at both LL & HL
Jitter Method | Improved , does not trigger OCP | Improved , does not trigger OCP | 
Max Frequency | 360 kHz | 500 kHz | Higher due to shorter ZCD blanking time
Programmable Trim | Limited | Yes | Optimize controller behavior
Package Availability | 8/9 Pin | 8/9 Pin SOIC | 
Notes: How does this device fit into the existing portfolio?
Is it directly replacing old technology? If so, what are the improvements?
Is it an extension of an existing product family?

## Slide 4
Collateral
Pricing
Datasheet
Click Here
Product Page
Click Here
NCP134x Design Tool
Click Here
Product Presentation
Click Here