## Slide 1: NCP45610/NCP45650 – ecoSWITCH Generation 3
Load Switch
August 2021
Notes: *Mandatory Slide*
Above information can be pulled from onsemi.com if needed.

## Slide 2: NCP45610/NCP45650 – ecoSWITCH Generation 3
Value Proposition
Product Family Overview
Applications
Features
Advanced Controller with Charge Pump
Integrated N-Channel MOSFET with Low RON
Soft-Start via Controlled Slew Rate
Adjustable Slew Rate Control
Power Good Output
Thermal Shutdown
Under Voltage Lockout
Over Current Protection
Input Voltage Range 1 V to 13.5 V
Extremely Low Standby Current
Load Bleed
This is a Pb−Free Device
Benefits
Reduce BOM part count
Energy Efficient
Reduce inrush current and protect system
Control inrush current
Allows the system to respond to faults
Protect the system in when temperatures are too high
Protects the system power supply faults
Protect the system against system faults
Wide voltage range supports many applications
Save power by disabling large parts of the system
Quickly discharge output voltage after shutdown
Safe and environmentally friendly
Notebook and Tablet Computers
Handheld & Mobile Electronics
Portable Medical Devices
Hard Drives
Peripheral Ports
The NCP45610 and NCP45650 series of load management devices provide a component and area−reducing solution for efficient power domain switching with inrush current limit via soft start. These devices are designed to integrate control and driver functionality with a high performance low on−resistance power MOSFET in a single package. This cost effective solution is ideal for power management and disconnect functions in USB ports requiring low power consumption in a small footprint.
Application Photos
Application Photos
System or Application Block Diagram
Application Photos

## Slide 3: Partial Device Table
ON Part # | Family Gen. | Package |  | Sample | RON TYP VCC=5V VIN=1.8V | RON TYP VCC=3.3V VIN=5V | VIN Min (V) | VIN Max (V) | IMAX (A) | Adj Dis-charge | Adj Slew Rate | Power Good Signal | Fault Protect (Default) | Reverse Current Protect | Adj Over Current Protect
NCP4543 NCP4545-x | Gen 1 |  | QFN18 3x3x0.9 | Now | 10.2mΩ 4.7mΩ | 12.2mΩ 5.9mΩ | 0.5 | 6 | 7.3 10.5 | Yes | Yes | No | No | No | No
NCP45520-x NCP45521-x | Gen 2 |  | DFN8 2x2x0.9 | Now | 9.5mΩ | 10.1mΩ | 0.5 | 13.5 | 10.5 | Yes | No Yes | Yes No | Yes | No | No
NCP45524-x NCP45525-x | Gen 2 |  | DFN8 2x2x0.9 | Now | 18.0mΩ | 18.8mΩ | 0.5 | 13.5 | 6 | Yes | No Yes | Yes No | No | No | No
NCP4540-x NCP45541-x | Gen 2 |  | DFN12 3x3x0.9 | Now | 7.7mΩ | 8.0mΩ | 0.5 | 13.5 | 14 | Yes | Yes | Yes | Yes No | No | No
NCP45560-x | Gen 2 |  | DFN12 3x3x0.9 | Now | 4.1mΩ | 4.3mΩ | 0.5 | 13.5 | 17 | Yes | Yes | Yes | Yes | No | No
NCP45610 | Gen 3 |  | DFN8 2x2x0.9 | Now | 14.0mΩ w/VIN = 1.0V | 14.5mΩ | 1.0 | 13.5 | 8.0 | No | Yes | No | Yes | No | Yes
NCP45650 NCP45651 | Gen 3 |  | DFN12 3x3x0.9 | Now | 5.0mΩ w/VIN = 1.0V | 5.3mΩ | 1.0 | 13.5 | 14.0 | No N/A | Yes | Yes | Yes | No | Yes
NCP45730 NCP45731 | Gen 4 |  | DFN8 2x2x0.9 | Q3 ’21 | 7.6mΩ* | 7.6mΩ* | 3.0 | 24.0 | 12.7* | Yes | Yes | No Yes | Yes | No | Yes
NCP45732 | Gen 4 |  | DFN10 3x3x0.9 | Q4 ’21 | 7.6mΩ* | 7.6mΩ* | 3.0 | 24.0 | 12.7* | Yes | Yes | No Yes | Yes | No | Yes
NCP45750 NCP45770 | Gen 4 |  | DFN12 3x3x0.9 | Now |  | 5.9mΩ 3.6mΩ | 3.0 | 24.0 | 10 20 | Yes | Yes | Yes | Yes | No | Yes
NCP45760 NCP45780 | Gen 4 |  | DFN12 3x3x0.9 Dual Flag | Now Q3 ’21 |  | 20.0mΩ* 13.7mΩ* | 3.0 | 24.0 | 8.0 6.3* | Yes | Yes | Yes | Yes | Yes | Yes
NCP45790 | Gen 4 |  | DFN14 4x4x0.9 Dual Flag | Now |  | 8mΩ | 3.0 | 24.0 | 8 | Yes | Yes | Yes | Yes | Yes | Yes
-X Available with Active-High (-H) or Active-Low (-L) EN pin
* Preliminary
Current as of August 2021
NEW
NEW
NEW
NEW
NEW
NEW
NEW

## Slide 4: Competitive Comparison

## Slide 5
Data Sheets
Click Here
Application Note
Click Here
Videos
Click Here
Evaluation Boards
Click Here
Collateral
Pricing
  Part NumberX: $0.00
    MPQ
    Package
  Part NumberY: $0.00
    MPQ
    Package
  Part NumberZ: $0.00
    MPQ
    Package
Can include trainings, videos, app notes, blogs, eval board, etc